## Slide 1: Performance Comparison of NVIDIA Accelerators with SIMD, Associative,& Multi-core Processors for Air Traffic Control Management
Alfred Shaker, Johnnie Baker, Gokarna Sharma at Kent State University
Man (Mike) Yuan at Hefei University of Technology (China)

## Slide 2: Our Primary Goal
A primary goal of this research is to simplify the difficult problem of scheduling by using alternate architectures
A system will be called deterministic (or predictable) if the time it requires to perform a specific constant time operation computation is always the same.
Earlier research has shown that scheduling can be dramatically simplified on deterministic systems
Asynchronous systems are usually highly non-deterministic, primarily due to the nondeterministic way their communications is handled.
Complexity results show that most real-time task scheduling is NP-hard and running time will increase exponentially as the problem size increases.

## Slide 3: A Quick Review of SIMD Architecture
The primary features of the SIMD are shown in the below diagram.
The hardware supporting the IS (instruction stream) is a processor that is normally called the control unit
The control unit compiles the program and broadcasts each step in the code to the PEs.
All active PEs execute each broadcast instruction in lock step (i.e., synchronously)
The execution of a SIMD execution is deterministic and execution time for programming language commands are usually given in their manuals

## Slide 4: Associative Processors (APs)
The AP is a SIMD with additional hardware that supports some very useful ATM capabilities such as broadcasting, associative searches, and maximum/minimum reductions in constant time.
Goodyear Aerospace designed and built the first AP (called the STARAN) explicitly for use in ATM in the late 1960’s and early 1970’s.
Goodyear demonstrated the STARAN ability to perform ATM using live radar to FAA in 1972 at Dulles Field.

## Slide 5: Associative Processors (cont)
A second generation STARAN called the ASPRO was built in the 1970’s by Goodyear.
  The US Navy purchased over 170 ASPROs and primarily used them in the E-2C Hawkeye AWACS planes for over 15 years
  Used for carrier-based airborne early warning radar surveillance and command and control processing [3,4]
Dr. Kenneth E. Batcher was the chief architect for the STARAN and a consultant for the ASPRO while a professor at Kent State.
  Ken Batcher received both the ACM/IEEE Eckert-Mauchly Award and the IEEE Seymour Cray award for his contributions to high performance computing.

## Slide 6: Air Traffic Management (ATM)
Also known as Air Traffic Control (ATC)
Perhaps the most well-known and widely discussed real-time application
Many ATM deadlines are hard deadlines, as missing them can be catastrophic in real-life situations
Different implementations of ATC have some minor variations in the period length and frequency of executions of the tasks.
The cycle times used by Goodyear Aerospace demonstration of the STARAN SIMD performing ATC in 1972 at Dulles Airfield were
  Major cycle length of 8 seconds
  Period length of 0.5 second

## Slide 7: Air Traffic Control Tasks (Off-line Scheduling) (Assumed Max. Nr. Aircraft: 14000)
ATC Tasks | Periods (sec) | Proc Time (sec)
1. Correlation & Tracking | 0.5 | 1.44
2. Cockpit Display | 1.0 | 0.72
3. Controller Display Update | 1.0 | 0.72
4. Aperiodic Requests (200/sec) | 1.0 | 0.4
5. Automatic Voice Advisory | 4.0 | 0.36
6. Terrain Avoidance | 8.0 | 0.32
7. Conflict Detection and Resolution | 8.0 | 0.36
8. Final Approach (100 runways) | 8.0 | 0.2
Total (all tasks in a period) |  | 4.52

## Slide 8: STARAN ATC Software
The off-line schedule used to execute these 8 tasks was designed prior to coding and implemented in the code
  This is possible since the STARAN is deterministic
  Every deadline was met during every execution of these tasks
  The required execution of these tasks requires less that one-half of the available time.
The implementation of these 8 tasks was a major part of the work of building the STARAN software used at Dulles Field
This code required only 4017 lines of assembly code and about 1600 lines of sequential code for the control unit.
In earlier work [2], we showed that the STARAN’s execution of ATM ran in linear time.

## Slide 9: Using NVIDA for ATM
Since NVIDIA devices are SIMD-like, we decided to implement the following three ATM tasks:
  Correlation and Tracking
  Conflict Detection
  Conflict Resolution
The sequential complexity of the first two tasks are the most compute intensive among the ATM tasks, since they are O(n2)
While the NVIDIA devices are not usually deterministic due to the actions of the scheduler, our implementation of these algorithms was designed to minimize any nondeterminism created by the scheduler
  For example, we only use global memory to avoid using cache.
We use a block size of 96 threads. As the number of aircraft increases, the number of blocks also increase.

## Slide 10: The Four CUDA Kernel Functions
TrackDrones
  Performs the Tracking and Correlation tasks to match as many radar points as possible with the “expected location” of the corresponding aircraft
  Moves each aircraft forward to its new location.
  A thread is assigned to handle each aircraft
CheckCollisionPath
  Executes both the Collision Detection task and the Collision Resolution task.
  Having both tasks in the same kernel function eliminates the additional memory used to store a second copy of the flight information for each aircraft and eliminates the cost of transferring additional updates.

## Slide 11: Kernel Functions (cont)
SetupFlights
  Called once at the beginning of the program to create aircraft in the airfield space with an initial location, direction of travel, speed, and altitude.
  The random number generator is used heavily in this kernel.
Generate RadarData
  Used to the simulate radar data normally obtained from radar towers each half-second period.
  Created by adding some noise to the “expected position” of each plane.

## Slide 12: Implementation of Correlation & Tracking
A thread is assigned to each aircraft, using the thread index (with respect to the grid) as the index for the aircraft.
The same process is used in assigning one thread to each radar location.
A box 1 nautical mile (nm) is placed around one aircraft and any radar that lies inside this box is initially matched with this aircraft
  This is repeated successively for each aircraft.
Above process is repeated again twice with larger boxes in order to attempt to match an remaining unmatched aircraft with an unmatched radar.
  First with boxes of size 2nm and next with boxes with size 4nm
Aircraft or radar with more than one match are marked as “’unmatched”
Aircraft with matching radar are moved to their radar location
Unmatched aircraft are moved to their “expected position”

## Slide 13: Collision Detection
Uses an algorithm due to Ken Batcher
  Checks each pair of aircraft for a potential collision
  The only way a collision can occur is if both aircraft are within a distance of 1.5 nautical miles of each other within the next 20 minutes in every dimension (i.e., x, y, and height) at exactly the same time
  The complex calculations used by this algorithm to check whether two aircraft are on collision course in are omitted

## Slide 14: Collision Resolution
When a collision of a pair of aircraft is detected, the collision detection algorithm is suspended until this collision is resolved
If the aircraft are still far apart, the best choice may be to postpone further action to see if the problem disappears
  One aircraft may be in process of changing directions
To remove the conflict, the path of one aircraft is rotated clockwise by an angle of 5 degrees.
If this new path does not remove the conflict, then rotate the original path of this aircraft counterclockwise by 5 degrees
This process can be continued by increasing the angle by 5 more degrees (to a maximum of 30 degrees) until this collision is resolved.
After a collision free path is found, it must be also shown to be collision-free with all other aircraft before being used.

## Slide 15: Experimental Results
All timings listed are the average of many identical multiple timings.
All of the ATM tasks are constant time computations.
The multiple timings of the NVIDIA executions of each specific task are identical, indicating that NVIDIA’s computations of the ATM tasks are essentially deterministic.
  This makes it possible for us to schedule the NVIDIA execution of ATM tasks using off-line scheduling
  The NVIDIA executions never missed a deadline
  These results were true for each of our NVIDIA devices
The execution graphs show that the NVIDIA devices are able to perform the executions in less time than the STARAN, the ClearSpeed simulation of an AP, and our multi-core (Intel Xeon 16 core)

## Slide 16: Experimental Results (cont)
The graph for the NVIDIA devices appears to be “almost linear”.
The MATLAB quadratic approximation for these curves have a very small coefficient for the quadratic term.
  If these curves are actually quadratic, then the quadratic term has little effect on the timings until the number of aircraft becomes extremely large.

## Slide 17: Future Work
Extend our NVIDIA timing of 3 tasks to include all 8 basic ATM tasks.
  Meeting all 8 deadlines is more challenging than meeting the deadlines for only 3 of the ATM tasks.
The clock speed and size of the different systems vary widely due to age and size.
  These timings would be more fair if the execution graph of these systems were normalized, based on the maximum throughput power of each system.
  Normalized curves would provide information about the efficiency of each system.
The implementation of the 8 ATM task on NVIDIA could be extended to provide ATM support for groups (swarms) of drones working in remote areas,

## Slide 18: Selected References
Man (Mike) Yuan, Johnnie W. Baker, and Will C. Meilander. 2013. Comparisons of Air Traffic Control Implementations on an Associative Processor with a MIMD and Consequences for Parallel Computing. J. Parallel Distrib. Comput. 73, 2 (2013), 256–272.
John A. Stankovic, Marco Spuri, Marco Di Natale, and Giorgio C. Buttazzo. 1995. Implications of Classical Scheduling Results for Real-Time Systems. Computer 28, 6 (June 1995), 16–25. https://doi.org/10.1109/2.386982
B. Parhami, “SIMD Machines: Do they have a Significant Future?,” Report on a Panel Discussion at Frontiers ’95, https://www.ece.ucsb.edu/~parhami/pubs_folder/parh95-can-simd-future.pdf
Cleveland 2018 Airshow, U.S. Navy E-2 Hawkeye Fly-By, The Electronic “Eyes of the Fleet”, http://www.clevelandairshow.com/in-the-air/u-s-navy-e-2-hawkeye-fly-by/